## Slide 1: Almost there...

## Slide 2: Admin
kit returns
  Friday, 5:00pm, Zeynep sent out detailed instructions
course evaluations
topics we covered – I’d love to get your thoughts
  design workshops
  electronics
  mechanics
  programming
  ESP 32 homework
  final project

## Slide 3: Admin
report
  Saturday is fine
final prep
  watch video
  read article
  there will be an essay question on the material

## Slide 4: So here’s a problem for you...

## Slide 5
You have a robot the navigates a warehouse to gather items. It starts at a specific location, drives to a bin in a given row, picks the item, and takes it to a place to be boxed. The warehouse is organized in rows, and each row is marked with a line that has a number of "intersections" to determine locations of bins.

## Slide 6
The number of rows and bins in each row are stored as follows:
int rowCount;
int binsPerRow[rowCount]; //array of bind in each row
Your robot has line following sensors and a function that returns true when it detects an intersection. It also has a function that can be called to command it to retrieve an item from a bin in a specified row. When it receives an "order," it sets the targetRow and targetBin variables and then drives to pick up the item. After doing so, it continues to the end of the row and then to the boxing area..

## Slide 7
class Robot
{
int targetRow;
int targetBin;
int rowCounter = -1; // counter to keep track of row
int binCounter = -1; // and bins
bool CheckIntersection(); //returns true when an intersection is detected
void LineFollow();
void TurnLeft();
void TurnRight();
void GrabItem(); //once the bin has been reached, call this to get the item
}
Robot myRobot;

## Slide 8: Part I
Write out a function, GetItem(), that drives to the bin, grabs the item and then drives to the boxing area. For this part, just write a “sequential” program that counts intersections (i.e., a simple for loop). GetItem() is not a part of Robot, so you’ll need to use proper syntax to call the functions in that class.

## Slide 9: Part II
Now write out a state machine that could be used to accomplish the tasks. In the notes from class, TURNING is a state.

## Slide 10: Part II
Now write out a state machine that could be used to accomplish the tasks.
  Identify the states

## Slide 11: Part II
Now write out a state machine that could be used to accomplish the tasks
  Identify the states
  Identify the events that cause you to change states

## Slide 12: Part II
Now write out a state machine that could be used to accomplish the tasks.
  Identify the states
  Identify the events that cause you to change states
  Identify the actions you need to take when you change states

## Slide 13: Can you write CheckIntersection()?

## Slide 14: Can you manage the handlers?
void HandleIntersection()
{
switch(state)
{
case DRIVING_TO_ROW:
case DRIVING_TO BIN:
case DRIVING_TO_END:
}

## Slide 15
class Robot
{
int targetRow;
int targetBin;
int rowCounter = -1; // counter to keep track of row
int binCounter = -1; // and bins
void RetrieveItem(int row, int bin); //commands robot to retrieve an item
bool CheckIntersection(); //returns true when an intersection is detected
void LineFollow();
void TurnLeft();
void TurnRight();
void GrabItem(); //once the bin has been reached, call this to get the item
}
Robot myRobot;